## Slide 1
1
ELT Instrumentation Development Mark Casali
Notes: 1

## Slide 2: contents
Status of Instrument Roadmap and Instrument information
Technology Development programme
Procurement Framework

## Slide 3: Instrument interfaces
Pre-Focal Station
M6
Phasing
Windshake
Multiple concepts
Extensive discussion
Draft ICD now available

## Slide 4: Instrument Status and information
Notes: 4

## Slide 5: The Baseline Roadmap
Instrument | Status
MICADO | For recommendation/approval by Committees
MAORY | For recommendation/approval by Committees
HARMONI/LTAO | For recommendation/approval by Committees
METIS | For recommendation/approval by Committees
ELT-MOS | Call for Proposals to be issued July 2015
ELT-HIRES | Call for Proposals to be issued July 2015
ELT-6 | Call for proposals in 2016
ELT-PCS | To proceed when technology is ready (2019)
Constr. budget
Ops budget

## Slide 6: Establishing Instrument Technical Specs
HARMONI
TLR
Budget,
Tech considerations,
Risks
METIS
TLR
MICADO
TLR
MICADO *
Tech Spec
MAORY *
Tech Spec
* In addition there will be an ESO-owned interface control document between MICADO & MAORY
HARMONI
Tech Spec
METIS
Tech Spec
Tech Spec preparation in final stages.

## Slide 7: HARMONI (+LTAO)
IFS spectrometer. PI : Niranjan Thatte
Univ of Oxford | UK
UK ATC | UK
CRAL | France
ONERA | France
Obs Marseille | France
IAC | Spain
CSIC | Spain
ESO | 

## Slide 8: HARMONI & LTAO
IFU spectrograph from 0.5 to 2.4 μm
3 spatial pixel scales
  From diffraction limited to coarse ”seeing limited” scale
Low (3000) medium (7000) high (20000) spectral resolution
Includes
  Non-sidereal tracking
  Single Conjugate AO mode
Statement of Work includes LTAO study to PDR. Led by LAM & ONERA. Draft technical specifications are part of deliverables
  Will go to construction when Phase II funding is confirmed

## Slide 9: MICADO
MCAO-corrected camera. PI: Ric Davies
MPIE | Germany
USM | Germany
MPIA | Germany
IoA Gőttingen | Germany
Nova | Netherlands
LESIA | France
Univ of Vienna & Linz | Austria
INAF (Padova) | Italy
ESO | 

## Slide 10: MICADO
Precision Imager with 2 pixel scales and >30 filters
  1-2 mas & 3-4mas
Includes fixed-format spectroscopy mode
Includes
  SCAO module (shared with MAORY)
  Non-sidereal tracking

## Slide 11: MAORY
INAF | Italy
INSU-IPAG | France
ESO | 
Multi-Conjugate AO module. PI: E.Diolaiti

## Slide 12: MAORY
Multi-Conjugate 6-laser AO system for MICADO + 1 auxiliary port
  Corrected field of 70” for MICADO and 2.5’ at Aux port
Designed for 2 internal DMs + M4 (3-layer correction)
Includes
  non-sidereal tracking
  SCAO module (shared with MICADO)

## Slide 13: First instruments AO-ready
MICADO
MAORY
HARMONI
LTAO

## Slide 14: First instruments poor seeing
MICADO
MAORY
HARMONI
LTAO
1’ field of view
Has coarse pixel scale
giving fov ~ 6x6”

## Slide 15: METIS
Mid-IR imager & spectrometer. PI: B Brandl
NOVA | Netherlands
CEA Saclay | France
ETH | Switzerland
KU Leuven | Belgium
MPIA | Germany
UKATC | UK
Univ of Vienna | Austria
ESO | 

## Slide 16: METIS
L,M,N,Qshort Imager and spectrometer
Imaging
  Minimum of 10 filters. 10x10” [20x20] field
  Coronagraphy
L,M Spectroscopy
  Low, medium, IFU/x-dispersed high resolution
N Spectroscopy
  Low and medium resolution
Includes
  SCAO and non-sidereal tracking

## Slide 17: Instrument schedule
Scope/cost/options discussed with ELT management, instrument teams, advisory committees, STC and ESC
STC reviewed/recommended proposal in April
FC approved expenditures in May
Council approved GTO in June
Agreement signatures expected in Sept/Oct

## Slide 18: First-light Construction phase
Preliminary design (2017)
  Followed by cost/scope review
Final design (2019)
Preliminary acceptance – Europe (2024)
Commissioning (2024)
Provisional acceptance – Chile (2026)
  Warranty period follows
Final acceptance (2028)

## Slide 19: Multi-Object Spectrograph and High Resolution Spectrograph
Equal priority. Will start when ready.
Top-Level Requirements prepared
RFI was issued
  Enabled ESO to confirm interest in community
  Enabled ESO to understand proposed scope
Discussions with STC, Council and internal management have refined strategy
  Go ahead with open call for proposals, including GTO allocation
  Set cash budgets to what is available in long term planning
  Adjust scope to fit
  Very limited possibilities for additional GTO

## Slide 20: Multi-Object Spectrograph and High Resolution Spectrograph
Current schedule
Preparation of Call for Proposals for Phase A studies
    Includes cash total for instruments + GTO awards
    Cash flow limited by ESO financial position
    Competitive proposals welcome
Call issued, July 2015
Phase A start in 2016
  1-2 year studies finishing with review
  Then decision on construction

## Slide 21: Technology Development Programme
Notes: 21

## Slide 22: Instrument Science Detectors
Instrument | Number of Det | Pixel format | Wavelength um
MICADO | 13-16* | 4kx4k | 0.8-2.5
HARMONI | 8* | 4kx4k | 0.95-2.45
 | 8 | 4kx4k | 0.47-0.95
METIS | 1 | 1kx1k | 5-14(28)
 | 6 | 2kx2k | 3-5
ELT-MOS | 6* | 4kx4k | 0.6-1.7
 | 6-8 | 4kx4k or 6kx6k | 0.37-1
ELT-HIRES | 3* | 4kx4k | 0.8-2.45
 | 5 | 9kx9k | 0.3-0.8
ELT-PCS | 4* | 4kx4k | 0.95-1.65
 | 8 | 4kx2k | 0.6-0.9

## Slide 23: Instrument science detectors
Visits/discussions with manufacturers ongoing
  Selex, Raytheon, Teledyne, Sofradir have been visited.
It is likely that single bulk order ($20-30M) for the 30+ detectors will give us best price/performance
Call for tender in late 2016
Crucial that we work on specifications closely with instrument teams
  Unified science-driven specifications if possible
First light with the H4RG bare mux

## Slide 24: HO deformable mirror systems
crucial for ELT instrumentation
  Currently in a very difficult situation
  MCAO
  PCS (Epics). >20,000 actuators
  Open-loop DMs
VLT AO instruments envisioned
  MCAO
  Extension to optical range
SPHERE DM

## Slide 25: WFS Detectors
eAPD HgCdTe devices (Selex)
  Major steps forward to very low read noise high-speed infrared detectors.
  For wavefront sensors, fringe trackers, possibly science observations
High speed CMOS (E2V)
  NGSD evaluation in lab at ESO
  Further revisions planned

## Slide 26: WFS Detectors
Pixel array (Refn pixels - 40 columns) | 1760x1680 (880x840 pixels in NGSD) - 5x6cm requiring stitched design (>> max. reticle 25.5x32.5mm)
Technology | Thinned backside illuminated CMOS 0.18µm – TowerJazz; APD5; 6 metal layers; MIM capacitor
Pixel pitch | 24µm
Pixel topology | 4T pinned photodiode pixel
Array architecture | 84x84 time coherent “sub arrays” of 20x20 (8x8 NGSD) pixels
NGSD / LGSD CMOS
Saphira
320x256
eAPD
HgCdTe
Gravity WFS

## Slide 27: Na Laser testing and performance
Tests of return flux as function of
Bandwidth
Polarisation
Auxiliary line strength
Annual variations
Collaboration with IAC on Obs.Teide

## Slide 28: Common Instrument Systems
Realtime computing
WFS cameras (focal plane, detectors, boards)
Science detector controllers
Attention must be paid to obsolescence and maintenance, and customisation.

## Slide 29: Infrastructure and Standards
PLC projects hosted within TecDev
  VLT PLC based instrument control. Workshop.

## Slide 30: Procurement Framework
Notes: 30

## Slide 31: New Guaranteed Time Policy for ELT
VLT policy was successful but GTO awards large and losing community support in recent years.
  GTO-FTE swap wrong incentive
New policy approved for ELT by Council on Dec 2014.
  GT allocation fixed at time of call for proposals (65 nights for normal instrument)
  GT return for cash contributions to be limited to exceptional circumstances. ELT at 300k/night.
  Up to 25% may be taken on another instrument

## Slide 32: Handling interface and design uncertainties
Recognising that much design and cost evaluation still needs to be done, that is..
  Interfaces still being finalized
  Design uncertainty remains
  Eg. MAORY design at early stage
  LTAO operation with HARMONI
  Cost estimation difficult (VLT not good guide)
ESO will conduct a review of cost and scope for all instruments following PDR. Revisions to cost and scope may result (under change control).

## Slide 33: “just in time” payments from ESO
ESO cash payments for instruments have increased substantially from 5M (VLT) -> 18M (ELT)
Improvements to smoothing cash flow and governance
  Cash payments to consortia for industrial procurements will be made close to calls for tender
  ESO will require regular reports on expenditure and will track cumulative expenditure

## Slide 34: ESO Project Participation
ESO participates as an associate member of each instrument team.
  Key responsibility is for detector and controller procurement and delivery
  AO system design and engineering support
Setting of standards for Instrument technology
  Eg Instrument Control
Common Instrument Systems

## Slide 35: Common Requirements and interfaces
First version of common instrument requirements has been released with input from teams and under final revision.
Interface document in final revision
  Provides clear interface description for instruments, role of telescope WF sensing, space envelopes, etc.
  Strong involvement of inst. teams
  No ideal solution. Compromise required. High-level decision taken. Further iteration planned in a version 2.

## Slide 36: summary
First three instrument agreements to be signed soon. Preliminary design starting early 2016.
Call for Proposals for Phase A studies for HIRES and MOS out soon.
Technology development under way to support the instrument programme

## Slide 37: End and questions